## Slide 1
Data Extraction Using Aerial Imagery: Not Just a Pretty Picture
Mapping Wildlife Habitat and Identifying Evergreen Forest with ArcGIS Spatial Analyst.
M. Keith Wethington
Fish & Wildlife Information System
Kentucky Department of Fish & Wildlife Resources
Daniel Vichitbandha
Gary Sprandel
Tammi Johnson

## Slide 3
Background/Problem
Quail research project involving KDFWR and University of Tennessee at Peabody WMA.
Request for ¼ acre resolution habitat mapping.
Patch size threshold for importance to quail habitat needs.
Roughly 1:2,500 scale.
Previous hand digitized maps at 1:8000 not sufficient.

## Slide 5
Challenges:
Short time frame (1 month)
Staff on other projects
Staff ability to photo interpret habitat types accurately
Large area (9,000 Acres)
Reclaimed surface mine, normal vegetation rules don’t apply
Difficult to differentiate ‘trees’ from ‘shrubs’
Topography altered, no elevation models

## Slide 6
Digitized at 1:8,000

## Slide 7
Approach:
Utilize existing high quality recent photography (2010 NAIP)
Use Image Analyst to allow software identification of Woody Vs Open habitat.
Create continuous raster dataset
  not discrete polygons of scrub-shrub/forest/and open lands
Generate raster dataset of woody and open pixels

## Slide 8
Methods:
Used Model Builder and Image Analyst
Identified and removed known features such as water, roads, developed areas.
Established ‘training sites’ for woody and open habitat
Multiple iterations that refined training sites
Used ‘Aggregate’ function to generate continuous data set

## Slide 9
Model Builder

## Slide 10
Clipped Aerial Photography

## Slide 11
Image Analyst Extension for ArcGIS
Requires ArcInfo license and Spatial Analyst Extension
Establish ‘training’ sites within imagery

## Slide 12
2010 NAIP Imagery
1 meter resolution

## Slide 13
Interactive Supervised Classification
Woody value 1, Open value 0
Discrete raster data set

## Slide 14
Aggregate combines 1m pixels into 10m pixels. Each 10m pixel is the ‘mean’ of the 100 input pixels.
Pixel values range from 0-100. Continuous raster data set

## Slide 15
Classification
Used Jenks Natural Breaks with 5 classes
(0 to 0.1) open habitat
(.847 to 1) forested
Classes in between ecologically scrub-shrub?
Species found there might be typical of a forest
Not functioning as forest on the landscape.
Where to define line between forest-shrub-open ecotone (edge)?

## Slide 17
Advantages
Currency (2010 imagery)
Precision (1 meter)
Allows raster analysis, nearest neighbor, etc
Scalable. Aggregate function allows any pixel size
Disadvantages
Complex procedure
Model Builder useful but can’t capture all steps (e.g., functions on toolbar)
Large files sizes
ArcGIS not a ‘raster friendly’ environment

## Slide 18
Conclusions
Augments human eye digitizing
  Still requires human inspection (we still matter!!)
  Removing roads and water is a manual process
  Software often confuses water and forest
Very sensitive to imagery quality
  Smoke from Paradise coal plant, clouds, etc
Capable of mapping woody vs. open habitat over large areas
Depending on research need can be overkill
  (1 meter resolution)
Potential for mapping cedar with leaf off imagery

## Slide 19
Peabody Ken Mine Site

## Slide 20
1 meter initial classification

## Slide 21
10 meter aggregation

## Slide 22
Identifying Cedar

## Slide 30
Potion of Kleber WMA

## Slide 31
Cedar areas identified for harvest by contractor

## Slide 32
Cedar areas identified by image analysis

## Slide 35
Cedar areas identified by image analysis

## Slide 36
Conclusions
Near infrared leaf-on imagery can help identify cedar stands
Very sensitive to image quality
Can not (yet) distinguish commercial Vs non-commercial
Could be useful for targeting traditional inventory
Image Analyst technique is probably overkill
Visual inspection and hand digitizing good enough